## Slide 1: CampusWatch x360
Team ID : GEN26-A0H-I014
Team Name : Data Alchemists
Domain : 2 – Energy, Mobility and Smart Infrastructure
Amrita Vishwa Vidyapeetham, Coimbatore Campus
Date: 11th October 2026

## Slide 2: Presentation Outline
Problem Statement
Problem Understanding
Existing Gaps & Challenges
Our Proposed Solution
Technical Approach
Innovation & Uniqueness
Feasibility & Scalability
Cost for Product
Use Cases
Impacts and Benefits
Sustainable Development Goals
Individual Member Contribution

## Slide 3: Problem Statement
How can a university reduce avoidable resource use while keeping essential campus services?
Electricity, water, rooms, meals and transport depend on the same campus activities. A decision that improves one service can create a shortage, delay or capacity conflict elsewhere.
CampusWatch x360 proposes a shared decision process that connects current evidences ,expected demand and operational constraints before recommending an action.
Research foundation: [1] Bonnet et al., 2002; [3] Antunes-Batista et al., 2026. Five-service integration is
our proposed design.
“An Al-powered campus system that predicts cascading impacts and recommends smarter decisions across interconnected university operations.”

## Slide 4: Problem Understanding
Users: campus administrators, facilities teams, room schedulers, hostel wardens, mess managers and transport coordinators. Students and staff depend on their decisions.
Causes to address : disconnected records, uncertain attendance, poorly mapped meters and changing event or service schedules.
Consequences: avoidable consumption, conflicting room choices, excess food preparation, queues and poorly timed trips.
Pilot context: begin with Amrita’s first-year academic-block electricity visualisation, then connect selected services with staff approval.
Campus resource context: [1] Bonnet et al., 2002. Causes and consequences above define the proposed pilot problem, not measured Amrita losses.

## Slide 5: Existing Gaps & Challenges
Research already supports | CampusWatch’s proposed extension
Activity-based energy and water analysis [1] | Link readings to campus activities and compare actions across services.
Leak analytics and connected water meters [2,5] | Combine water balance, storage, inspection and pumping constraints.
Room optimisation and radar passage counting [3,4] | Combine room suitability, demand forecasts and service dependencies.
Deployment challenges: data quality, uncertain demand, sensor coverage and conflicting commitments. Forecast attendance does not establish live vacancy.

## Slide 6: Our Proposed Solution
Five specialist engines, coordinated by one Campus Brain
System | Evidence and proposed decisions
Energy | Meter readings: forecasts and load shifts.
Water | Flow and tanks: loss and reserve checks.
Space &Occupancy | Timetables and counts: suitable room plans.
Food | Meal records and waste: cooking quantities.
Mobility | Trip logs and counts: capacity and timing.
Proposed digital twin : connect staff-validated assets. The Brain checks shared constraints, requests operator approval and verifies outcomes. Room plans must accommodate authorised participants.

## Slide 7: Technical Approach
Blueprint + asset IDs Staff verify meter links
Meters + campus records Readings and service data
Validate + PostgreSQL Time, IDs, units, quality
Gateway / CSV / API MQTT / HTTPS
Worker: five forecast engines Ranges, evidence and candidate actions
Campus Brain Constraints + joint plans
Dashboard + digital twin Approval + outcomes
observed
outcomes
Proposed Tech StackWeb: React, TypeScript, Three.js
API: FastAPI + Python worker
Data: PostgreSQL
AI: scikit-learn, rules, OR-Tools
One backend and worker. Optional OR-Tools. Modbus where supported. Unknown readings stay unknown.

## Slide 8: Innovation & Uniqueness
Five forecasts + current evidence
no Revise
plan
Feasible together?
yes
Rank feasible plans Benefit, cost, uncertainty
and staff effort
Operator approval Measure outcomes
Proposed differentiator: evidence-aware coordination across five services, with a measurable decision trail. Validate against independent modules and current practice.
Five systems, one Campus Brain: Coordinates energy, water, space, food and mobility through one shared decision process.
Tests the consequences before recommending: Compares complete plans and checks how each action affects other services.
Knows what to check next: Reuses existing data and requests targeted information only when it could change the decision.
Adapts across departments: A change in attendance or bus arrivals can update room allocation, cooking and resource schedules together.
Measures the combined impact: Evaluates resource savings and service quality under one intervention record, avoiding double-counted benefits.

## Slide 9: Feasibility & Scalability
Starting point: electricity visualisation for first-year blocks. Five-system forecasts and control recommendations remain proposed.
Bounded pilot: one academic block and a mapped hostel water zone, with selected mess and bus records. Reuse compatible meters and staff data.
Validate, then trial: labelled simulations, read-only observation, baseline comparison and operator-approved actions.
Scale by configuration: reusable adapters and campus IDs, local calibration, access controls and explicit operating constraints.
Risks and response: buffer network outages, flag stale data, reconcile meter coverage and check forecast errors. Optional entrance radar requires a separate pilot.
[1] Bonnet et al., 2002; [3] Antunes-Batista et al., 2026; [4] Ślesicka et al., 2026. Forecast occupancy is not live presence. No universal sensor count or accuracy is assumed.

## Slide 10: Cost for Product (Optional)
Proposed three-month pilot: INR 75,000 planning allocation.
Illustrative budget, subject to site survey and quotations. Assumes compatible existing meters, campus connectivity and student development.
Pilot allocation | Amount (INR)
Gateways and device interfaces | 15,000
Selective sensing or meter rental | 20,000
Installation and calibration | 20,000
Hosting and connectivity for three months | 5,000
Contingency | 15,000
Scope: selected block/hostel monitoring; Food and Mobility use records. Student labour and laptops are in kind. Excludes commercial development, bulk meter replacement, major civil work, automatic controls and full-campus rollout.

## Slide 11: Use Cases
Evidence
1. Event peak
600 people; 650 seats.
145 kW; limit 120 kW.
Bus 12:15; meals 12:30.
Proposed decision
Shift 30 kW pump. Earlier: 110 kW.
Event: 115 kW.
40 − 24 − 10 = 6 m3.
Checks and outcome
Check tank + pump. 25-min transfer: 12:40. Reject: meal deadline. Verify peaks and service.
2. Water discrepancy
Inlet 20; use 14 m3. Storage rises 5 m3. Unexplained: 1 m3.
Check data + meters. Inspect suspect branch. Repair confirmed faults. Residual ̸= proven leak.
Maintain water supply. Compare water balance over matched periods after the repair.
3. Timetable change
60 authorised;
42 forecast.
14:00 unconfirmed. 65-seat room available.
Confirm new time. 65 seats: accept.
45 seats: reject. Align other services.
Check room + capacity and service deadlines. No confirmation:
keep the current plan.
Illustrative. Case 1: one electrical boundary; all guests at meals by 12:30. Water: 40 m3 after pumping, upper demand 24 until next feasible refill, reserve 10. Verify total kWh: shifting a peak
alone is not an energy saving.
Not supplied | Not supplied

## Slide 12: Impacts and Benefits
Expected benefit | Evidence the pilot will collect
Lower avoidable resource use | Adjusted kWh, peak kW, water volume and food waste per meal.
More reliable campus services | Capacity conflicts, water reserves, meal shortages, passenger waits and late arrivals.
Better operational decisions | Useful alerts, staff effort, approved actions, completed tasks and net operating benefit.
How we test the innovation
Compare current practice, independent modules and the shared planner on equivalent scenarios. Record net benefits and service failures under one intervention ID. Results may be positive, negative or inconclusive.
Proposed outcomes. Evaluation: U.S. DOE FEMP, Measurement and Verification.

## Slide 13: Sustainable Development Goals (SDGs)
Intended contribution to specific UN SDG targets
SDG Number | Target Number | Goal Name | Connection
SDG 6 | Target 6.4 | Clean Water and Sanitation | Track losses and protect water supply.
SDG 7 | Target 7.3 | Affordable and Clean Energy | Reduce avoidable kWh per comparable activity.
SDG 12 | Target 12.3 | Responsible Consumption and Production | Forecast meals. Measure waste per meal.
Local project indicators. Energy efficiency requires improved energy use per equivalent service; moving demand to another time alone does not prove it.
United Nations DESA: Goal 6, target 6.4; Goal 7, target 7.3; Goal 12, target 12.3.

## Slide 14
Individual Member Contribution
Member | Contribution or responsibility
Prajit Anand | Team coordination and presentation
Mohit Vaswani | Visual design and documentation
Tanishq Borah | Solution planning and feasibility
Sriram S | Research and problem analysis

## Slide 15
Yukti ID
Yukti ID
IR2026-1051093